## Slide 1: Development of High-Order Discontinuous Galerkin Method Within OpenFOAM
Liyang Xu1, Xinhai Xu2, Xuefeng Yuan3, Xiaoguang Ren2, Shuai Ye1
1State key Laboratory of High Performance Computing,
NUDT, Changsha, China
2Innovation Institute for Defence Science and Technology, the Academy of Military Science (AMS), China
3Advanced Institute of Engineering Science for Intelligent Manufacturing, Guangzhou University, China
Email: HopeFOAM@163.com
2017/07/24
Notes: Hello everyone, today I am gona show you our work, the development of high order discontinuous galerkin method within openfoam.

## Slide 2: Outline
Motivation for high order schemes
Basic principles of DG-FEM
Implementation within OpenFOAM
  design philosophy and framework
  user interfaces
  support of curved mesh
Preliminary results
Future work
Notes: This report mainly contains five part. Firstly, gets look at the motivation for high order schemes

## Slide 3: Motivation
Complex realistic problem simulation
  Wake and vortex flows
  LES/DNS
Other Challenges
  Complex geometries
  Multi physics and many scales
Notes: For realistic problems, the industrial applications especially, is very complicate and hard mainly caused by turbulence. Here are images of airfoil and delta wing. Wake and vortex flow will generate from the surface when flow past the geometries. To simulate these problem, we need LES or DNS method. Other challenges such as complex geometries, multi physics and many scales.
In the simulation of these problems, the mesh need to be very dense to obtain satisfied results. However, the computational cost will increase dramatically.

## Slide 4: Motivation
2nd order accuracy may not be enough
  much more points to achieve given accuracy
  limitation of computation cost and scalability
Require advanced numerical methods
  high performance, high scalability and high-order accuracy
Notes: Nowadays, finite volume is the most popular method in Computational fluid dynamics. But in some circumstances, the 2nd order accuracy may not be enough. In complex problems, we need much more points to achieve given accuracy comparing to high order methods. At the edge of Moore's law about to come to its end, we tend to use multi-core and parallel program to get higher computation ability. But this is very hard. For larger problem, we need more processors. Due to the limitation of scalability, it is not practical to get idea parallel efficiency. It may even be slower with more processors because the communication overhead.
So, we are looking for advanced numerical methods, which are high performance, high scalability and high order accuracy especially.

## Slide 5: Motivation
Definition of high-order method
Cost evaluation
  given accuracy and specific period of time
    2m = order of the scheme
    d = dimension of the problem
truncation order > 2
Notes: We define the high order methods are those with truncation order higher than 2rd order.
Here are the approximate cost evaluation equation illustrates relation between memory and cpu cost with order, dimension and given error limit.
For a critical case ,and the error limit, dimension, and accuracy order set. Let us analysis the cpu costs. For cases with high accuracy required, the second term is much larger than the first term and will the majority. With the order in the denominator分母 of exponent指数.
So, the overall overhead will drop dramatically when using high order.

## Slide 6: Motivation
Comparison of common methods
DG-FEM = FVM + FEM
Notes: Here are the comparison of common differencing methods taken from Heathevan and Warboton’s book, including FDM, FVM, FEM and DG. The tick means suited while a cross means not suited. Here we have 5 criterion, including complex geometries, high order accuracy and hp-adaptivity, Explicit semi-discrdte form, conservation laws and elliptic problems. FDM , we can see, not suits for complex geometries but good at other 4 criterion. The FVM is hard to achieve high order accuracy, while FEM fail in explicit semi-discrete form. DG is a combination of FVM and FEM, and inherits their advantages in discretization. For this reason, we choose DG as the ideal approach.

## Slide 7: Motivation
High-order methods are hard to implement and use
  DG is flexible (unstructured grid)
  Organization of DG is similar to FVM
OpenFOAM
  2nd FVM
  well designed framework and user interface
  excellent tool chain
Bring DG to

## Slide 8: Basic principles of DG-FEM
Nodal DG-FEM
  Piece-wise polynomial
  Element k:
    —basis function
    -- nodal value of field
    -- number of basis points
……
……
Element
Face
Notes: Continuous function represented by piece-wise polynomials. Each cell is represented separately.
The neighboring cells are not indeed separate, they are combined by flux.

## Slide 9: Basic principles of DG-FEM
Consider PDE system
Flux calculation
  Riemann solver to stabilized the discretization
Cell Integration
Face Integration
Notes: Let’s consider a PDE system.
Solution at the interfaces is multiply defined and discontinuous
With this constraints, the whole computational domain forms a linear system.

## Slide 10: Design principle and framework
OpenFOAM Basic
Data Structure
Scalar
Vector
Tensor
GeometricField
dimensionedField
polyMesh
polyPatch
fvMesh
fvPatch
volScalarField
volVectorField
……
fvPatchField
Point
Face
Cell
lduMatrix
fvMatrix
FVM Related
Data and Methods
Fvc::div
Fvc::grad
Fvm::div
Fvm::grad
Fvm::laplacian
User Interface
DSL(fvm::div(phi, u)==0)
Control Dictionary
Scalar
Vector
Tensor
Notes: Next I will talk about how we design the DG with OpenFOAM and out framework.
In my understanding, OpenOAM mayinly have 3 levels. The bottom is basic data structure.
The middle level is the finite Volume related data structure and methods.
The top level is user interfaces and other physical models. The user interface refers to DSL and control dictionary.

## Slide 11: Design philosophy and framework
Design philosophy
  Reuse the framework and data structure
  Keep consistent with the user interface
  Inherit the pre and post processing tools
  Add a separate DG source package
    High order DG discretization
    High performance
    High extensibility, runtime selection

## Slide 12: Design principle and framework
External Libs
PETSc
BLAS
Metis
Scotch
VTK
SLEPC
DSL(dgm::div(u, u)=0)
Control Dict
DG Discretization
Kernel
DG Related
Methods
Nodal Base
dgMesh
dgField
dgMatrix
DG tools
Boundary Conditions
Limiters
Flux Calc Schemes
dgc/dgm
Schemes
hp Controlers
Matrix
Solvers
Interfaces
polyMesh
polyPatch
Scalar
Vector
Tensor
Point
Face
Cell
GeometricField
dimensionedField
User Interface
OpenFOAM Basic
Data Structure
Notes: We add a separate level called DG discretization kernel.
We rewrite the DG related methods

## Slide 13: User interfaces
DSL in DG (Euler equation)

## Slide 14: User interfaces
Control dictionary
  system/controlDict, system/decomposeParDict
    nearly the same with original OFM
  system/dgSolution
  system/dgSchemes

## Slide 15: Support of curved mesh
Curved mesh is critical to achieve high order convergence rate
  6 cells cavity with 6th basis
Notes: Wo also provide support to curved mesh. Bassi Proved that curved mesh is critical to achieve high order convergence rate. For 2nd order method this won’t be a problem. Here is a example of curved mesh and straight side mesh.

## Slide 16: Support of curved mesh
Implementation and configuration
based on codeStream

## Slide 17: Preliminary results
Isentropic vortex problem, inviscid
h (256) h/2 (1024) h/4 (2028)
Results with 256 cells and 3rd basis
High order post processing

## Slide 18: Preliminary results
Convergence order test
  Euler solver with Roe flux
N | Error in ρ |  |  |  | Error in ρu |  |  | 
 | h | h/2 | h/4 | Rate | h | h/2 | h/4 | Rate
1 | 1.101E-02 | 3.344E-03 | 8.759E-04 | 1.83 | 2.361E-02 | 7.182E-03 | 1.793E-03 | 1.86
2 | 3.481E-03 | 3.621E-04 | 3.972E-05 | 3.23 | 6.384E-03 | 8.060E-04 | 9.689E-05 | 3.02
3 | 6.523E-04 | 5.471E-05 | 3.173E-06 | 3.84 | 1.610E-03 | 1.226E-04 | 7.141E-06 | 3.91
4 | 2.352E-04 | 8.808E-06 | 3.690E-07 | 4.66 | 5.187E-04 | 1.866E-05 | 8.533E-07 | 4.62
5 | 6.597E-05 | 1.477E-06 | 5.505E-08 | 5.11 | 1.388E-04 | 2.695E-06 | 1.591E-07 | 4.88
6 | 2.530E-05 | 2.675E-07 | 1.232E-08 | 5.50 | 4.675E-05 | 4.760E-07 | 3.837E-08 | 5.13
OFM-FVM | 1.340E-02 | 7.209E-03 | 3.039E-03 | 1.07 | 3.466E-02 | 1.733E-02 | 6.945E-03 | 1.16
Notes: This is the convergence order test results.
A popular misunderstanding about high order method is that it is computational expensive. Maybe under the same mesh, the high order methods is slower. but this comparison is not fair, because the high order methods obtain more accurate results. So, here we gonna to see the computational cost under the same error limit.

## Slide 19: Preliminary results
Error-Cost test
Notes: Compare OFM and DG N=1
Compare the slop factor with different N
Extend the line of FVM, when high accuracy is need, the FVM costs much more computation.

## Slide 20: Preliminary results
Double Mach Problem, inviscid, 10 Ma
  Euler solver with 1st order basis, LF flux and gradient limiter
  To utilize high order basis, need high order limiter
Notes: To test the ability of Dg to handle complicate problem.

## Slide 21: Preliminary results
Flow past cylinder, Re=100
  INS solver with pressure projection method
  1840 cells with 3rd basis
  Curved mesh in cylinder patch

## Slide 22: Future work
What already support
  High order DG space discretization (up to 8)
  OFM compatible user interface
  Inviscid Euler & INS solver
  High order curved mesh
To be developed
  3D basis extension
  hp adaption
  High order limiter, shock capturing
  LES models
  Performance optimization